Scrutineering Check List

PLEASE CHECK THE FOLLOWING LIST BEFORE THE EVENT, SIGN AT THE BOTTOM TO CONFIRM, AND HAND IN AT CHECK IN TO CONFIRM YOUR CAR IS SAFE TO BE ON THE TRACK. IF YOUR CAR IS SUBSEQUENTLY FOUND NOT TO COMPLY, YOU MAY BE ASKED TO PACK UP AND LEAVE IMMEDIATELY OR YOU WILL BE DENIED ENTRY UNTIL FIXED.

|  | EXTERNAL | Pass | Fix |
| --- | --- | --- | --- |
| 1 | Tyres- type, condition and metal valve caps |  |  |
| 2 | Stop lights Working/ Headlights Taped (clear film preferred) |  |  |
| 3 | Wiper / Washers work |  |  |
| 4 | Wheels secured firmly (check nuts) |  |  |
| 5 | Windscreen-check for clear visibility and no cracks |  |  |
| 6 | No Oil leaks |  |  |
|  | BOOT |  |  |
| 7 | Battery-safely secured / Battery Triangle Affixed |  |  |
| 8 | No loose objects |  |  |
|  | ENGINE BAY |  |  |
| 9 | Check for fluid leaks |  |  |
| 10 | Check - brake fluid level and evidence of leaks |  |  |
| 11 | Battery - safely secured / Battery Triangle Affixed |  |  |
| 12 | Accelerator - Must be free of binding, throttle return springs safely attached |  |  |
| 13 | No loose objects |  |  |
| 14 | Secondary bonnet strap if required |  |  |
|  | INTERIOR OF CAR |  |  |
| 15 | Steering wheel - secure, grip not loose |  |  |
| 16 | Seat belts - secured, sound operation and condition |  |  |
| 17 | Front seats - secured firmly |  |  |
| 18 | Brake pedal -NOT low or spongy |  |  |
| 19 | Fire extinguisher – 1kg minimum, secured by metal bracket fixed securely, in reach of driver and less than 3 years old |  |  |
| 20 | Doors - locks functioning and able to be opened from inside |  |  |
| 21 | No loose objects |  |  |
| 22 | Helmet - complies with AS1698 specifications, no physical damage |  |  |
|  | UNDER CAR |  |  |
| 23 | Suspension - check for correct operation |  |  |
| 24 | Exhaust - check for secure mounting and noise limit (75db) |  |  |

Signed by entrant: ……………………………………… Car ………………………………..

Name (print):…………………………………………Entry Number: ………………………..